## Slide 1: Chapter 7.3 Communication Protocols
2012.11.18

## Slide 2: The Five-Layer TCP/IP Internet Protocol Hierarchy
Layer | Name | Examples
5 | Application | HTTP, SMTP, FTP
4 | Transport | TCP, UDP
3 | Network | IP
2b | Logical Link Control | PPP, Ethernet Data Link Layer
2a | Medium Access Control | Ethernet
1 | Physical | Modem, DSL, Cable Modem, Wi-Fi, 3G

## Slide 3: Physical layer protocols (1)
Govern the exchange of binary digits across a physical communication channel, such as a fiber-optic cable, copper wire, or wireless radio channel.
The goal is to create a “bit pipe” between two computers for communication
101010
101010
pipe

## Slide 4: Data Link Layer (2)
Medium access control protocols (2a)
  Determinate how to arbitrate ownership of a shared line when multiple nodes want to send message at the same time
    Centralized manner through a single master control node (rarely used, too slow)
    Contention based approach (e.g. Ethernet)
      How to deal with collision? (resend after a random time r)
  Ethernet’s control is distributed, each node makes its own decision when to listen, when to send and when to wait. The failure of one node does not affect the operation of any other node in the network.

## Slide 5: Data Link Layer
Logic link control protocols (2b)
  Now, with medium access control protocols, think of node A and B are directly connected by a physical link.
  packet M: sequence-number(unique), start of packet (SOP), end of packet (EOP) , error-check
SOP | Sequence-number (ID) | message | Error-check | EOP

## Slide 6: Data Link Layer
Logic link control protocols (2b)
  ARQ algorithm (automatic repeat request)
  Acknowledgement message (ACK)
    Node A maintains a copy of the packet, wait node B return a ACK, then discard its local copy, or resend if not received ACK from node B
  ACK is itself a message and can be lost or damaged during transmission
  The ARQ algorithm guarantees that every message sent (eventually) arrives at the destination

## Slide 7: Network Layer (3)
Creating a universal addressing scheme for all network nodes (every nodes agree to use this scheme)
Delivering messages between any two nodes in the network (how to be fast?)
Internet protocol (IP)
  32-bit IP address, often written as four 8-dit numeric quantities in the range 0-255
Domain name system (DNS)
  Which is a massive database that convert from a symbolic host name to its 32-bit IP address
  Local name server (remote name server, another, … etc )
  Routing algorithm (Dijkstra’s shortest path algorithm )

## Slide 8: Transport Layer (4)
Problem: many application programs in one machine, when a message comes in, how do we know which program it is for and where to deliver it?
Port number
  Assigned to programs to remember which programs goes with which port
  The transport protocol at the destination node examines the newly arrived message to determine which program should get it, based on the port number field inside the message
Notes: When a message comes in, how do we know which application program it is for and where to deliver it?

## Slide 9: Transport Layer (4)
Transport control protocol (TCP)
  Deal with errors and reliability (IP don’t guarantee the arriving of every message sent and the order)
  Create a high-quality, error-free, order-preserving, end-to-end delivery service
    1. establish a connection between two programs at the source and destination node
    2. inform each other of the impending message exchange
  TCP use the same ARQ algorithm
    Hold the later message until the earlier message arrive
Notes: When a message comes in, how do we know which application program it is for and where to deliver it?

## Slide 10: Application Layer (5)
The application layer protocols are the rules for implementing the end-user services provided by the network
Uniform Resource Locator (URL)
Hyper-text transfer protocol (HTTP)
Notes: When a message comes in, how do we know which application program it is for and where to deliver it?

## Slide 11
Dijkstra’s Algorithm

## Slide 12
Have a great Thanksgiving